AgonLight2-HvIO
User Manual
Rev.1.0 October 2023	olimex.com
# Introduction to AgonLight2-HvIO

AgonLight2-HvIO is Open Source Hardware board designed to work with AgonLight2.
It has these features:
- Four Solid-State-Relays SSR capable working on 240VAC with 1 A loads connected to AgonLight2 GPIO outputs
- SSR are with zero cross switching noise free
- Four opto isolated 240VAC inputs connected to AgonLight2 GPIO inputs
- Status LEDs for each output and input
- Status LEDs for 3.3V and 5V power supply of AginLight2
- Two Dallas DS18B20 temperature sensor inputs capable to work with SNS-TMP-DS18B20
- Dimensions 100x70 mm

## Order codes for AgonLight2-HvIO:

AgonLight2-HvIO	AgonLight high voltage IO board
SNS-TMP-DS18B20	temparature sensor
CABLE-IDC34-15CM	not available yet cable between AgonLight2 and AgonLight2-HvIO
# HARDWARE

## AgonLight2-HvIO layout:
AgonLight2 GPIO connector

Power supply status LEDs

Temperature Sensors DS18B20

High voltage Outputs
High voltage Inputs
Power supply Live and Neutral
## AgonLight2-HvIO schematic

The schematic of AgonLight2-HvIO is on GitHub. On the next page there is picture of it.

## AgonLight2 GPIO connector:

## AgonLight2-HvIO temperature sensors connector:

# SOFTWARE:

## Reading the Inputs and Writing to the Outputs:

The outputs are assigned as follows:
OUT1 → PC4
OUT2 → PC5
OUT3 → PC6
OUT4 → PC7

The inputs are assigned as follows:
IN1 → PC0
IN2 → PC1
IN3 → PC2
IN4 → PC3

Port-C Data Direction Register is at address 159. To make port Input 1 should be written in the corresponding bit, to make it Output 0 should be written.
To make PC0-3 as inputs and PC4-7 as outputs the following basic command should be executed:
PUT 159 , %00001111
Port-C Data Value register is at address 158, so to read the Port-C status you can use:
PRINT GET(158)
and to set OUT1 = HIGH
PUT 158, %00010000
to set OUT1 = LOW
PUT 158, %00000000

Here is sample test program:
10 PC_DR% = &9E
20 PC_DDR% = &9F
30 PC_ALT1% = &A0
40 PC_ALT2% = &A1
50 PD_DR% = &A2
60 PD_DDR% = &A3
70 PD_ALT1% = &A4
80 PD_ALT2% = &A5
90 PUT PC_DDR%, &F
100 PUT PC_ALT1%, &00
110 PUT PC_ALT2%, &00
120 PUT PD_DDR%, &FF
130 I=0
140 Input=0
150 PCD = GET(PC_DR%)
160 Input = Input OR ((PCD EOR &F) AND &F)
170 PRINT "PCD="; PCD; " Input=";Input; " I="; I
180 I=I+1
190 IF (I<10) THEN GOTO 150
200 PUT PC_DR%, Input*16
210 Temp = GET(PD_DR%) AND &C0
220 IF (Temp = &C0) THEN GOTO 130
230 PUT PC_DR%, (GET(PC_DR%) AND &3F) OR ((GET(PD_DR%) AND &C0)EOR &C0)
240 PCD = GET(PC_DR%) AND &F
250 IF (PCD=15) THEN GOTO 230 ELSE GOTO 130
# Revision History
Revision 1.0 October 2023	initial